## Slide 1: Fruit2U Banana Dehydrator
Team Members:
Ash Thomas
Aaron Seemungal
David Sehrt
Kwasi Darkwah

## Slide 2: Agenda
Background
Problem Statement & Solution
Requirements
Use Case Model
System and Requirements Validation & Verification
Functional Architecture
Concept Exploration
Analysis
WBS
Cost Estimation
Conclusion
1.
2.
3.
4.
5.
6.
7.
8.
9.
10.
11.

## Slide 3
Need
Food Wastage
Distribution Challenges
Global Hunger
Global Warming
Food Shortage
Background

## Slide 4
Need
Food Wastage
Distribution Challenges
Global Hunger
Global Warming
Food Shortage
Background

## Slide 5
Problem Statement
Food Wastage
Retail Groceries
Produce
Bananas
Develop an equipment to prepare, dehydrate and package surplus bananas for transport to food banks.
Goal: Reduces landfill and provides food to the hungry.
Solution
Short spoilage time and perishability lead to bananas being major contributors to produce waste [1].
Problem Statement and Solution

## Slide 6: Preliminary Concept

## Slide 7: Context Diagram
NSH
Grocery stores provide infrastructure and bananas.
Store Employees are operators.
NSH
Food Banks benefit from output of Fruit2U System.
Fruit2U
Logistics Companies
Retail Grocery
(Customer)
Food banks
Regulatory bodies
Store Employee (EQ User)
Maintenance / Sanitation team
Notes: Customer VS user

## Slide 8
Requirements
The Fruit2U shall detect Class I through Class VII ripe bananas autonomously
The cutting component shall direct the flow of peeled bananas for slicing
The dehydrator shall be able to desiccate a fixed mass of banana pieces within a single cycle
The equipment shall be constructed using materials that meet regulatory requirements for food compatibility
The Package system shall screen incoming bananas for pathogens
Customer Requirements
Derived requirements

## Slide 9
Customer Requirements
Derived Requirements
Requirements were captured from the Customer. (e.g. RFQ, interviews)
ConOps helped refine Customer needs.
High level requirements were derived from Customer requirements.
Requirements

## Slide 10
Use Case Model
Inspection
Authority
1. Prepare
2. Cut
3. Dehydrate
4. Package
5. Inspect
Grocery Store Employee
Food Bank
Logistics Operators
System Boundary
Fruit2U System
Key
Out
In
Retail Groceries
/
System Bounds: Fruit2U is the equipment used to dehydrate bananas. It is not the dehydrated bananas.
Grocery Store employees will interface with Fruit2U to produced dehydrated bananas.
Inspectors will need occasional access to the Fruit2U to ensure food safety is met.
Logistic companies receive the output of the Fruit2U (dehydrated bananas) who pass the product to Food banks.
Internal interaction
External interaction

## Slide 11: Agenda
Background
Problem Statement & Solution
Requirements
Use Case Model
System and Requirements Validation & Verification
Functional Architecture
Concept Exploration
Analysis
WBS
Cost Estimation
Conclusion
1.
2.
3.
4.
5.
6.
7.
8.
9.
10.
11.

## Slide 12
System Validation & Verification
Adapted from INCOSE diagram

## Slide 13
System Validation & Verification
Requirements | Verification Method
Detect Class I through Class VII ripe bananas autonomously. | T- Simulation and testing of detection function
Direct the flow of peeled bananas for slicing. | D- Demonstration of transfer lines
The dehydrator shall be able to desiccate a fixed mass of banana pieces within a single cycle. | A- Analysis of heat chamber and volumes. T- Prototype testing.
The equipment shall be constructed using materials that meet regulatory requirements for food compatibility. | I- Inspection and qualification of components used in equipment.
The Package system shall screen incoming bananas for pathogens. | T- Simulation and testing of microbe detection capability.
T Test | I Inspection | D Demonstration | A Analysis
Adapted from INCOSE diagram
Baseline Verification
– Are we building it right?
Baseline Validation
– Are we building the right thing?

## Slide 14: Functional Architecture

## Slide 15: Functional Architecture – Tree Diagram

## Slide 16: Functional Flow Block Diagram
Bananas Enter
Bananas Exit

## Slide 17
Prepare
Manual Sorting
Vision System
Chemical
X-Ray
Cut
Cutting edge- blade, saw Blade
Waterjet
Laser
Wire
Dehydrate
Electric dehydrators
Conventional Oven
Microwave Oven
Solar Oven
Package
Aseptic Packaging
Cans
Bottles
Vacuum Bags
CCD cameras
X-Ray Inspection​
Manual Inspection​
Batch Inspection​
Inspection​
Technology Market Survey
Concept Exploration

## Slide 18: Concept Exploration
Explored potential technologies for each function based on customer need/requirements
Combined identified technologies in morphological matrix
Exploration of TRLs included (TRL used NASA standards)
CUT |  |  |  | 
Characteristic Alternatives | Cutting edge - Blade, saw | Waterjet | Laser | Wire
Cost | 9 | 4 | 3 | 7
Reliability | 8 | 5 | 3 | 7
Maintainability | 8 | 5 | 4 | 7
Longevity | 8 | 4 | 3 | 7
Energy efficiency | 8 | 4 | 3 | 5
Slice Speed | 8 | 8 | 9 | 5
TRL | 9 | 7 | 2 | 6
Illustrative (subsystem) example

## Slide 19: Agenda
Concept Exploration
System and Requirements Validation & Verification
Functional Architecture
Background
Problem Statement & Solution
Requirements
Use Case Model
Analysis
WBS
Cost Estimation
Conclusion
1.
2.
3.
4.
5.
6.
7.
8.
9.
10.
11.

## Slide 20: Morphological Matrix
Morphological Matrix fed into system architectures.
Each Architecture was verified for compatibility of technologies.
Architecture 1 | Architecture 2 | Architecture 3 | Architecture 4
Cost-Focused | Process Time | User-Friendliness | Maintainability
Vision System Sorting | X-Ray Sorting | Vision System Sorting | Chemical Sorting
Cutting edge-Blade, saw | Laser | Cutting edge-Blade, saw | Cutting edge-Blade, saw
Solar Oven | Microwave Oven | Electric Dehydrators | Conventional Oven
Vaccuum Bags | Vaccuum Bags | Aseptic Packaging | Cans
Batch Inspection | Batch Inspection | CCD Cameras | Manual Inspection

## Slide 21: Design Model
Architecture 1 | Architecture 2 | Architecture 3 | Architecture 4
Cost-Focused | Process Time | User-Friendliness | Maintainability
Vision System Sorting | X-Ray Sorting | Vision System Sorting | Chemical Sorting
Cutting edge-Blade, saw | Laser | Cutting edge-Blade, saw | Cutting edge-Blade, saw
Solar Oven | Microwave Oven | Electric Dehydrators | Conventional Oven
Vaccuum Bags | Vaccuum Bags | Aseptic Packaging | Cans
Batch Inspection | Batch Inspection | CCD Cameras | Manual Inspection
Which architecture to down select?

## Slide 22: Design Model-Analysis
First pass-evaluation / preliminary analysis
Equal weighting across Criteria
Pugh recommends A3: User Friendliness Architecture
Drawbacks:
The Pugh Matrix provided a general (unsatisfactory) result. Did not provide confidence in a decision.
Criteria | DATUM | Architecture 1 | Architecture 2 | Architecture 3 | Architecture 4
Cost | 3 | + | - | - | +
Energy Efficiency | 3 | + | - | + | S
Reliability | 7 | S |  | + | -
Maintainability | 5 | + | - | + | +
Durability | 7 | S | - | S | S
Performance | 6 | - | + | + | -
TRL | 9 | S | - | - | +
Process Stability | 4 | - | + | - | S
Food Safety | 8 | - | + | + | -
Capacity | 8 | - | S | + | -
Seal Quality / Ingress | 9 | S | S | - | -
Ease of Implementation | 6 | + | - | S | +
Sum of Postives |  | 4 | 4 | 6 | 4
Sum of Negatives |  | 4 | 6 | 4 | 5
Sum of Sames |  | 4 | 2 | 2 | 3
Weighted Sum of Positives |  | 17 | 25 | 37 | 23
Weighted Sum of Negatives |  | 26 | 33 | 25 | 38
Overall Score: |  | -9 | -8 | 12 | -15
PUGH Matrix Legend |  |  |  |  | 
S | Standard |  |  |  | 
+ | Better than |  |  |  | 
- | Less than |  |  |  | 

## Slide 23: Prioritization Matrix
Criteria relative importance | Safety | User Friendly | Process Time | Maintainability | Total across rows | % of Grand Total
Safety |  | 1.00 | 1.00 | 5.00 | 7.00 | 0.32
User Friendly | 1.00 |  | 0.20 | 1.00 | 2.20 | 0.10
Process Time | 1.00 | 5.00 |  | 5.00 | 11.00 | 0.51
Maintainability | 0.20 | 1.00 | 0.20 |  | 1.40 | 0.06
Column Total | 2.20 | 7.00 | 1.40 | 11.00 | 21.60 | 1.00
KEY | 0.1 Extremely less important | 0.2 Significantly less important | 1 Equally important | 5 Significantly more important | 10 Extremely more important
Prioritization Matrix helps generate weights for TOPSIS Analysis.

## Slide 24: TOPSIS
Quantitative metrics | Weight | Cost Focused | Process Time | User-Friendliness | Maintainability
Product Cost ($) | 30% | $7,000 | $20,000 | $15,000 | $12,000
Processing Time (hrs) | 20% | 7 | 3 | 6 | 9
Food Safety Rating (1-10) | 12.5% | 8 | 10 | 9 | 8
Power Consumption (kW-hrs) | 10% | 5.2 | 11.8 | 6.2 | 9.2
Ease of Implementation Rating (1-10) | 10% | 2 | 5 | 9 | 6
Capacity (sq ft) | 7.5% | 45 | 50 | 64 | 40
Repair and Maintenance Rating (1-10) | 5% | 7 | 3 | 7 | 10
Reliability Rating (1-10) | 5% | 7 | 7 | 8 | 5
Closeness to Ideal |  | 0.627 | .392 | 0.510 | 0.482
Rank |  | 1 | 4 | 2 | 3
TOPSIS was performed for more quantitative evaluation
Prioritization Matrix informed weights, but not for all TOPSIS criteria
  Cost was considered most important criterium
TOPSIS and PUGH results diverged; TOPSIS recommends A1: Cost-Focused.

## Slide 25: Work Breakdown Generation
WBS leveraged MIL-STD-881E (281-page standard!)
Appendix K- Common Elements most applicable to the Fruit2U System.
Section 3 explained 12 common elements
Tailored these Common elements to Fruit2U: Systems Engineering, Program/Project Management, Training, Facilities, Data Support, Standard Equipment, etc.

## Slide 26: Work Breakdown Structure
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*MIL-STD Appendix K Elements Captured in WBS.
Other Elements identified as important to Fruit2U.

## Slide 27: Agenda
Analysis
WBS
Concept Exploration
System and Requirements Validation & Verification
Functional Architecture
Background
Problem Statement & Solution
Requirements
Use Case Model
Cost Estimation
Conclusion
1.
2.
3.
4.
5.
6.
7.
8.
9.
10.
11.

## Slide 28: Cost Estimate: Bottoms-Up from WBS
WBS Work Packages allowed for an accurate estimation of project development costs.
Lognormal is conservative with right shifted PDF.
Beta has a PDF influenced by expertise.
Distribution | Typical Application
Gaussian (normal) | Used when there is an equal chance of high/low occurrence.
Lognormal | Used when there is no better info is available.
PERT-Beta | Used when there is an Expert opinion available. It emphasizes the “most likely” value over the minimum and maximum estimates
Uniform | Used when the likelihood of outcomes is unknown or unclear. Useful in situations in which you have a minimum and maximum estimate available, but no other information
Fixed | Used when the value is unlikely to vary.
*PDF= Probability Distribution Function
  Top-down, Analogous, and Expert Judgement were not feasible approaches.
  Distributions were modeled as fixed, range, lognormal, and PERT-Beta

## Slide 29: Cost Estimation
Proprietary GT PMASE Matlab code was altered for the Fruit2U System.
Systems Engineering required 14% of costs.
The 80% Cumulative Percentage (CDF) was $340K. (Range $165K-$765K)
Has elements of lognormal distribution (result of inexperienced conservative estimate with long tails)

## Slide 30: Conclusions
Fruit2U appears to be a viable solution to combat food waste and tackle systemic hunger.
The Fruit2U team successfully applied a Fundamental Systems Engineering development approach. System Verification and Validation is still needed.
  ASE6002 and other future courses would be essential to further develop Fruit2U through a deeper understanding of Systems Design and Analysis.
MBSE may be employed for further insight into Fruit2U and decision-making.
System Evaluation and Path Forward
Key Takeaway and Learnings
Difference between customer and system requirements.
Selection of the right tool for analyses.
Inhibit the excitement to jump straight into design.
There is an ideal balance between work put into quantitative analysis and the strength of the outputs for decision-making.
As always…systems is a team sport!

## Slide 31: Questions?
Conclusion

## Slide 32: Thank You!
Conclusion
Special thanks to Brian for his continued mentorship and guidance